## Slide 1
DDCA • DESIGN & SIMULATION
GRAY CODE
TO BINARY
A 4-bit combinational converter using cascaded XOR logic
G3
1
G2
1
G1
0
G0
1
→
Gray input
Notes: Introduce the topic and the goal: converting four Gray-code input bits into the equivalent ordinary binary output. Explain that this is a combinational logic project built from XOR gates. The slide assignments are balanced across four presenters, three slides each.

## Slide 2
MEET THE TEAM
DDCA • GRAY CODE TO BINARY
PRESENTER 1 | 02
I. Deekshitha - 2620040021
S. Kavya - 2620040022
M. Sai Karthik - 2620040008
GR. Srinidhi - 2620040054
Section 8 • Replace the four name placeholders
Notes: Introduce all four team members and assign the speaking sections. Presenter 1 handles slides 1–3; presenter 2 handles 4–6; presenter 3 handles 7–9; presenter 4 handles 10–12. Replace each name placeholder before class.

## Slide 3
WHY GRAY CODE MATTERS
DDCA • GRAY CODE TO BINARY
PRESENTER 1 | 03
A SENSOR CAN READ THE WRONG VALUE
WHEN MANY BITS SWITCH TOGETHER.
BINARY CHANGE
011
→
100
3 bits change
GRAY CHANGE
010
→
110
1 bit changes
Gray code reduces ambiguous transitions in position sensing.
Notes: Compare the transition between decimal 3 and decimal 4. Binary changes from 011 to 100, so all three bits change. Gray code changes from 010 to 110, only one bit. If a sensor samples during a transition, fewer changing bits can reduce the chance of reading a misleading intermediate value. Gray code is especially useful in position sensing.

## Slide 4
GRAY CODE VS ORDINARY BINARY
DDCA • GRAY CODE TO BINARY
PRESENTER 2 | 04
BOTH REPRESENT THE SAME NUMBER. THEIR BIT PATTERNS FOLLOW DIFFERENT RULES.
DECIMAL
BINARY
GRAY
0
000
000
1
001
001
2
010
011
3
011
010
Adjacent Gray values differ in one bit. That single rule defines the code.
Notes: Binary and Gray code represent the same integer sequence, but their bit patterns are different. In the first few values, binary counts in the familiar way. Gray code changes only one bit between successive values: 000, 001, 011, 010. This property distinguishes Gray code and motivates the converter.

## Slide 5
PROJECT OBJECTIVE AND SCOPE
DDCA • GRAY CODE TO BINARY
PRESENTER 2 | 05
WHAT THE CONVERTER DOES
Takes a 4-bit Gray input and produces the equivalent 4-bit binary value.
INPUT
G3 G2 G1 G0
→
PROCESS
Direct MSB + 3 XOR stages
→
OUTPUT
B3 B2 B1 B0
Combinational logic: the output depends on the current input only.
Notes: State the project objective and input/output boundary. The input is four Gray bits and the output is four binary bits. The process is combinational: there is no clock, memory, or stored previous value. Only the currently applied input pattern determines the output.

## Slide 6
WHAT WE NEED TO BUILD
DDCA • GRAY CODE TO BINARY
PRESENTER 2 | 06
DESIGN CHECKLIST
4
one-bit Gray input pins
3
two-input XOR gates
4
one-bit binary output pins
Goal: derive the equations, explain the signal flow, and verify examples.
Notes: These are the main components and goals of the project. Each input and output pin carries one bit. Three two-input XOR gates implement the conversion. The goal is not only to assemble the circuit, but also to explain why the equations work and verify the results with examples.

## Slide 7
THE CONVERSION RULE
DDCA • GRAY CODE TO BINARY
PRESENTER 3 | 07
START AT THE MOST SIGNIFICANT BIT. MOVE TOWARD THE RIGHT.
B3 = G3
copy the first bit
B2 = B3 ⊕ G2
previous binary ⊕ next Gray bit
B1 = B2 ⊕ G1
carry the result forward
B0 = B1 ⊕ G0
repeat for the final bit
⊕ = exclusive OR (XOR): 1 when inputs differ; 0 when they match.
Notes: Explain the recurrence. The most significant bit is copied directly: B3 equals G3. Then each lower binary bit is computed by XORing the previous binary result with the Gray bit at that position. XOR outputs 1 when inputs differ and 0 when they match. This makes the computation cumulative from left to right.

## Slide 8
WALK THROUGH ONE CONVERSION
DDCA • GRAY CODE TO BINARY
PRESENTER 3 | 08
WORKED EXAMPLE
GRAY INPUT
1 1 0 1
G3 G2 G1 G0
B3
G3 = 1
1
B2
1 ⊕ 1 = 0
0
B1
0 ⊕ 0 = 0
0
B0
0 ⊕ 1 = 1
1
BINARY OUTPUT
1 0 0 1 = 1001
The new bit is always calculated from the result above it.
Notes: Work the input 1101 one bit at a time. B3 is copied from G3, giving 1. For B2, calculate 1 XOR 1, which gives 0. For B1, calculate 0 XOR 0, giving 0. For B0, calculate 0 XOR 1, giving 1. The binary output is 1001. Emphasize that every step uses the previous binary result.

## Slide 9
WHY THE XOR CHAIN WORKS
DDCA • GRAY CODE TO BINARY
PRESENTER 3 | 09
A SIMPLE RULE REPEATED FOUR TIMES
01
B3 starts the binary result
The most significant bit is shared by Gray and binary.
02
Each XOR recovers the next bit
A change between adjacent Gray positions toggles the binary state.
03
The result feeds the next stage
The chain preserves all earlier information as it moves right.
No clock • No memory • One direct wire + three XOR gates
Notes: This slide explains the pattern behind the equations. B3 establishes the starting binary state. Every Gray bit tells us whether the binary state should toggle, which is exactly what XOR expresses. Each newly calculated binary bit becomes the reference for the next stage. The design is small and combinational, so it has no clock or memory.

## Slide 10
WHERE GRAY CODE IS USED
DDCA • GRAY CODE TO BINARY
PRESENTER 4 | 10
POSITION SENSING
A rotary encoder reports the angle or position of a rotating shaft.
ROTATING SHAFT
changes position
↓
GRAY-CODE SENSOR
one bit changes
↓
CONVERTER
forms binary value
↓
CONTROLLER
uses position data
WHY IT HELPS
Only one bit changes between adjacent positions.
Fewer simultaneous transitions can reduce ambiguous sensor readings.
Notes: A common example is a rotary encoder on a motor shaft or control knob. As the shaft turns, the sensor reports position in Gray code. Because adjacent positions change one bit at a time, transitions are less likely to produce an ambiguous reading. The converter then supplies ordinary binary position data to a controller.

## Slide 11
KEY TAKEAWAYS
DDCA • GRAY CODE TO BINARY
PRESENTER 4 | 11
THE PROJECT IN THREE IDEAS
01
Gray code changes one bit between adjacent values.
02
Binary is recovered with a direct MSB connection and cascaded XOR.
03
Position systems can convert Gray readings into binary for processing.
Notes: Summarize the key ideas: Gray code limits adjacent changes to one bit; the converter reconstructs binary through a direct most-significant-bit connection and a cascade of XOR operations; and this conversion is useful in position systems. Invite the class to explain why XOR is a natural operation for detecting whether a bit changes.

## Slide 12
DDCA • SECTION 8
THANK YOU
Notes: Thank the class and invite questions. Presenter 4 can close by returning to the real-world purpose: Gray code helps reduce ambiguous transitions in position sensing, and the converter turns those readings into binary for further processing.